## Slide 1: GPU Computing with CUDA
COMP 445

## Slide 2: GPU: Massive fine-grain data parallelism
CPU
A relatively small amount of very fast, complex cores
Individual and shared cache and large main memory
Programming model is to split out many data elements per core
GP-GPU
Thousands of simpler cores
Different memory layout
Different architecture
Programming model is one thread in one core works on one data element

## Slide 4
CPU memory is larger, GPU memory has more bandwidth
CPU and GPU memory are separate, connected by an I/O bus (traditionally PCI-e)
Any data transferred between the CPU and GPU will be handled by the I/O Bus
The I/O Bus is relatively slow compared to memory bandwidth
The GPU cannot perform computation until the data is within its memory
Host
Device
Kernel function runs on the device after data transfer
Data must be transferred to/from the host memory

## Slide 5: Different Architectures & Nomenclature
Streaming processor, or core

## Slide 6: Different Architectures & Nomenclature
32 cores/SPs per SM
Each core running code gets registers
Some cores/SPs are for special calculations
SIMD (single instruction, multiple data):
When running instructions of a program, each SP in one SM is executing the same instruction
Warp scheduler: runs the code on an SM

## Slide 7: CUDA Programmming
Normally we will have large arrays of data
They can be managed in two ways:
Programmer manages (not used any more on newer cards):
  allocate memory on host and device,
  copy data to device,
  Compute on device,
  copy data back to host
Programmer specifies “unified memory”
  Allocate once as memory that will reside on device and host
  Compute on device

## Slide 8: Programming Model
Taken from this blog post
Simplest version:
1D blocks of threads
inside
1D grid of blocks
CUDA:
Programmer defines sizes:
Blocks per grid
Threads per block
Dimensions
NVIDIA compiler:
CUDA
2D and 3D are possible

## Slide 9: NVIDIA Architecture
Programming model of threads is somewhat related to this

## Slide 10: CUDA Programming Model
y
x
z
Overall dimensions:
gridDim.x (y, z)
blockDin.x (y, z)
Programmer accessible per-thread values:
Indexes of the block a thread is in:
blockIdx.x. (y,z)
Indexes of the position of the thread in a block:
threadIdx.x (y, z)
From these, a unique overall thread id can be calculated

## Slide 11: CUDA Programming Model
y
x
z
Overall dimensions:
gridDim.x (y, z)
blockDin.x (y, z)
Programmer accessible per-thread values:
Indexes of the block a thread is in:
blockIdx.x. (y,z)
Indexes of the position of the thread in a block:
threadIdx.x (y, z)
Programmer determines unique thread id from 0 to (N x L)-1 like this: ((my block index in the x direction) * (number of threads in a block)) + my thread index in the block I'm in threadNumber = (blockIdx.x * blockDim.x) + threadIdx.x
Blocks per grid
Threads per block

## Slide 12
y
x
z

## Slide 13
y
x
z

## Slide 14: NVIDIA Architecture
Programming model of threads is somewhat related to this:
It’s best to have block sizes that are a multiple of 32
Each block specified maps to an SM
This hasn’t changed:
32 SPs/cores per SM

## Slide 15: CUDA Programming
Define a kernel function that will run on the device
__global__ void test1DGridKernel(int val) {
…
}
Call it by specifying how many blocks and how many threads per block (simplest case 1D grid of 1D blocks)
// 1 block of 32 threads goes to 1 SM
test1DGridKernel<<<1, 32>>>(10);

## Slide 16: CUDA Programmming
Normally we will have large arrays of data
They must be managed in two ways:
Programmer manages:
  allocate memory on host and device,
  copy data to device,
  Compute on device,
  copy data back to host
Programmer specifies “unified memory”
  Allocate once as memory that will reside on device and host
  Compute on device